     Student Name: Gökay Gülsoy
     Student Number: 270201072

        -CENG312-ASSIGNMENT 3 IP, ICMP, NAT, DHCP-

        1.)
        a.) When we look at the packet traffic “Fragmentation needed” ICMP messages

        are triggered in case amount of data that should be carried by datagram exceeds

        the maximum amount of data can be carried within the datagram.

        b.) When endpoints receive the “Fragmentation needed” message endpoints can divide

        or in other words fragment datagram into smaller IPv4 packets. To identify fragements

        16-bit field is used as an identification field and this identification field is copied to

        fragmented packet header so that on the destination side receiver will be able to

        reassemble the fragments that belong to a particular frame. In the packet traffic there

        is a problem related to fragmentation, because even though endpoint with IP address

        62.177.254.141 has received ICMP message “Destination unreachable (Fragmentation

        needed)” three times it was not able to perform fragmentation. (Figure 1 and 2)

Figure 1: Fragmentation problem in the traffic

Figure 2: Reassembly operation on fragments is done according to id fields

        2.)
        a.) In the packet capture Info column, there is an information saying that

        “Fragmented IP protocol” with fragment’s offset number. (Figure 3)

        b.) Purpose of IP fragmentation is to divide large datagrams into smaller packets

        which does not fit into a single datagram previously. Later, fragments will be

        reassembled at the destination according to identification fields.

        c.) When we look at the line numbers 3,4, and 5 fragments with the ID=2d00

        are all reassembled into number #6 frame. In the lines 7,8, and 9 fragments with

        ID=3100 are all reassembled into number #10 frame. In the lines 11,12, and 13

        fragments with ID=2e00 are all reassembled into number #14 frame. In the lines

        15,16, and 17 fragments with ID=3200 are all reassembled into number #18 frame.

        In the lines 19,20, and 21 fragments with ID=2f00 are all reassembled into number #22

        (Figure 3 and Figure 4)

        frame. In the lines 23,24, and 25 with ID=3300 are all reassembled into number #26.

        ç.) If we look at the line numbers 3,4, and 5, fragments which have ID=2d00 belong to

        to frame with number #6. Each Fragment has a total length of 1500, so total

        length is 4500. We can also compute the original packet size by using offset values.

        First packet’s offset is 0 and second packet’s offset is 1480, so data length of first

        packet should be 1480. Second packet offset is 1480 and third packet offset

        is 2960, so data length of second packet is 1480. Third packet also has the

        data length 1480, so total data length is 4440 and also each fragment has 20

        byte header field so total 60 bytes for headers. Indeed 4440+60 = 4500 is the

        original IP packet length which conforms to total length information in Wireshark

        bottom panel. (Figure 4 and Figure 6)

        d.) For the fragments whose ID’s are 2d00, 2e00, and 2f00 Time to live field is

        32 whereas, fragments whose ID’s are 3100,3200, and 3300 have Time to live field

        value 128. So TTL value is different for some fragments. Reason that’s why TTL

        value for some fragments is longer than others can be attributed to importance of

        fragment, may be some fragments some fragments are given more importance due to

        role of data they carry. (Figure 5)

Figure 3: Calculating original packet length with help of offset information

Figure 4: Total length and header length fileds of fragments

Figure 5: Time to live fields of fragments with ID's 2d00,2e00,2f00 is 32

Figure 6: Time to live fields of fragments with ID's 3100,3200,3300 is 128

        3.) If we look at the line number 8 we can see in the packet comments section that “IPv6

        packets are encapsulated in IPv4” this is the method of tunelling and encapsulation where

        IPv6 datagrams are embedded inside IPv4 datagram to sent to destination address. Also

        when we look at the Internet protocol version 4 part below the packet capture table we

        can see that Protocol field is also IPv6.

Figure 7: IPv6 packets encapsulated inside IPv4 datagrams

        4.)
        a.) We can observe two ICMP message types as a result of executing traceroute

        command from terminal. First one is Type 11 which gives the time exceeded message when

        a router receives a datagram with TTL of 0 or 1. So by using this TTL value infinite

        routing loops are prevented. Routers can not forward a datagram that has a TTL of 0 or 1

        and packet is dropped. ICMP message of code 0 indicates Time-to-live became equal

        to 0 during transit not during reassembly. Second is Type 3 ICMP message which

        indicates that the router cannot find the destination network. Code 3 which says “port

        uncreachable” indicates that trasport layer protocol we are attempting to communicate

        is not available on the arriving side.

        b.) As a result of executing traceroute google.com command, intermediate network

        devices are same in both cases because when we look at the hop IP addresses, in the

        Wireshark and in the output of traceroute they are same. It is intuitive to get same

        intermediate device IP addresses because we have captured packets during the same

        traceroute execution. (Figure 10)

        c.) Routers with IP addresses given inside blue rectangle in the screenshot below have

        have been sent 3 packets. Routers with the IP addresses given inside the red rectangle

        have been sent 1 packet. (Figure 8 and Figure 9)

Figure 8: Routers with IP addresses given inside blue rectangle have been sent 3 packets

Figure 9: Routers with IP address given inside the red rectangle have been sent 1 packet

Figure 10: traceroute command output and the hops along with their IP addresses and packets they received

        NAT SECTION

        1.) NAT protocol stands for Network address translation which allows all devices

        inside local area network to share just one IP address as far as outer networks are

        considered , so all datagrams leaving from local network share same NAT

        IP address, but they are distinguished by different port numbers. The mapping

        between datagram source IP address and NAT IP address, is implemented in the

        form of NAT table. NAT protocol also helps IPv4 address exhaustion because just

        one IP address is needed from ISP for all devices in local network.

        2.) When we look at the lan-packets screenshot below, scenario might be as follows:

        host with IP address 10.142.154.239 and destination with IP address 8.8.8.8 are

        located in the same local area network and host is trying to establish a TCP connection

        with server whose IP address is 8.8.8.8. When we look at the wan-packets screenshot

        below, scenario might be as follows: host with IP address 136.102.83.11 and destination

        with IP address 8.8.8.8 are located in different networks and host is trying to establish

        a TCP connection with server whose IP address is 8.8.8.8. This scenarios can be related

        to NAT protocol as follows: Actual IP address of host may be 10.142.154.239 inside it’s

        local area network but let’s say as in WAN scenario server with IP address 8.8.8.8 is

        located outside the LAN and any host when connecting to any server in LAN is using

        IP address 10.142.154.139, but when server for which host is going to establish

        connection is outside the LAN, there is a NAT router which translates IP address of

        host from 10.142.154.239 to 136.102.83.11. Thus when server sends response to

        host it sees it’s NAT IP which is 136.102.83.11 not it’s actual local network IP

        address which is 10.142.154.239. (Figure 11 and Figure 12)

Figure 11: Scenario in which host with IP address 10.142.154.239 and destination with IP 8.8.8.8 in same LAN

Figure 12: Scenario in which host with IP address 136.102.83.11 and destination with IP 8.8.8.8 in different LANs

        DHCP SECTION

        1.) ipconfig /release command will inform the DHCP server that we don’t want to

        use previously assigned IP address any larger and we release it. After releasing the

        previously assigned IP address we can request new IP address from DHCP server

        with ipconfig /renew command. Note: As I am using UBUNTU distribution of

        Linux, I have used dhclient program for releasing and obtaining new IP address

        with DHCP which is equivalent to ipconfig program on Wİndows.

        2.) When we look at the packet capture on Wireshark 1 DHCP packet was captured

        for the release command, 4 DHCP packets were captured for first renew command.

        2 DHCP packets were captured for second renew command.

        3.) If we look at the Wireshark packet capture when when I made two new requests

        respectively to DHCP server both newly assigned IP address in both situtation

        were same as we can see in the below screenshots. In both situations requested IP

        address was 192.138.0.1, but this may not always be the case, IP address can

        differ from previous one.

        4.) When we look at the packets as a result of first renew command, we can see

        four different DHCP message types which are DISCOVER, OFFER, REQUEST,

        and ACK respectively. DHCP DISCOVER message is sent by client to locate DHCP

        server when client attempts to connect network for the first time. DHCP OFFER

        message is sent by server in response to DHCP discover message of client, and it caries

        configuration information along with the new IP address. DHCP REQUEST message is

        sent by server. Finally DHCP ACK message is sent by server to acknowledge DHCP

        REQUEST message sent from DHCP client. After receiving DHCP ACK message client

        obtains configuration parameters including new IP address.

        5.) For first dhclient command (which is equivalent to piconfig /renew on Windows)

        common option fileds to all packets are as follows: subnet mask which defines the subnet

        IP of computer that belongs to particular LAN, IP address of DHCP server, and DHCP

        message type option which indicates the sending purpose of DHCP packet that I have

        explained detaily in the previous question (4) it can be of type DISCOVER, OFFER,

        REQUEST, ACK, etc.. to indicate what client wants from DHCP server and DHCP

        servers response.

Figure 13: DHCP Discover message

Figure 14: DHCP Offer message type

Figure 15: DHCP Request message type

Figure 16: dhclient command equivalent to ipconfig in Wİndows for releasing IP address and obtaining new IP address

Figure 17: DHCP ACK message for second dhclient command (same as ipconfig /renew)