Student name: Gökay Gülsoy
Student number: 270201072

        -CENG312-ASSIGNMENT 2 TCP and UDP-

        Q1-) Sender has sent packet with SYN to server and server has returned SYNACK to

        sender, but when we look at the rest of this traffic we can see that third packet of the

        handshake never arrived. Each duplicate ACK is querying for ACK 1 with sequence

        number 1 in the handshake, but as the client has two different packets with sequence

        number 1, this issue never solved.

Figure 1: assignment2-tcp-1 third packet in handshake never arrived

        Q2-) Firstly server sends an ACK 1 for a packet with sequence number 1, then client with IP

        address 192.168.0.104 sends a packet with sequence number 6349, but then server has sent

        three duplicate ACKs for a packet with sequence number 1. Then client used fast-retransmission

        to send the packet with sequence number 1, this indicates that it was a lost packet with high

        probability. Then client retransmits packets with sequence numbers 1461, 2921, 4381, 1

        respectively. Server ACKed the packet with sequence number 1, and client retransmitted

        packets with sequence numbers 4381 and 5841. Server has returned cumulative ACK 4381, then

        client has sent packet with sequence numbers 7301 and 8761. Then server returned cumulative

        ACK 6861 and client has sent packets with sequence numbers 10221, 11681, and 12621. Server

        Server then sent three duplicate ACK for cumulative ACK 6861 and as no ACK

        has returned from client, client fast-retransmitted packet with sequence number 6861

        in order to avoid congestion which may be caused by a lot of retransmissions. Finally

        server retransmitted cumulative ACK 6861. In summary we can see that there were a lot

        of packet loss and in order to avoid congestion, fast-retransmissions used so that no more

        than three duplicate ACK’s will accumulate and this avoids congestion.

Figure 2: assignment2-tcp-2 a lot of packet loss and retransmission scenerio

        Q3-) When we monitor the traffic we can see 41 instances of “TCP ZeroWindow” segment

        This means that due to lack of available buffer space, server is not able to receive any more

        data. We can see that server sends a TCP segment with “TCP Window Full” 9 times. During

        that time interval to keep TCP connection open even if no packet can be received, server also

        sends TCP segment with “TCP-keep-alive” info.

Figure 3: assignment2-tcp-3 “TCP Window Full”

Figure 4: assignmet2-tcp-3 “TCP Zero Window segment”

Figure 5: assignment2-tcp-3 "TCP Keep Alive"

        Q4-a-1) We can see from Time Sequence Stevens Graph that sequence numbers of

        packets sent start with low sending rate, but after that it has increased exponentially until

        approximately 4.127 second. After 4.193 second we can see that there is a congestion up

        until to 4.418 second, then again sequence number of packets sent started to inrease at low

        rate, after that it continued with exponential increase until approximately 5.983 second after

        which increase switched to linear.

Figure 6: assignmet2-tcp-4-a-1 Time Sequence Stevens Graph

        Q4-a-2) In the Wİndow Scaling Graph we can see that receiving window is a flat

        green line and it denotes the window’s size at a given time, so relation between

        receiving window and bytes out (which denotes bytes in flight) is that number

        of bytes out can never exceed current receiving window size. If receiving window

        scales, then maximum number of bytes out can scale accordingly.

Figure 7: assignment2-tcp-4-a-2 Window Scaling Graph

        Q4-b-4) We can see the slow start behavior in Time Sequence Stevens graph and Window

        Scaling Graph. At 0.00011 second sent packet number is 3, if we look at the 5.123 second sent

        packet number reaches to 926, so number of packets sent per second is approximately 176.481

        in time interval 0.00011 to 5.123 second. If we look at the 67.68 second, number of last

        packet sent was 18805. if increase rate had remained same, then number of last packet

        sent would have been 11944 but actual packet number sent at 67.68 second 18805. This

        inidcates that packet sent rate has increased over time.

Figure 8: assignment2-tcp-4-b-4 Time Sequence Stevens Graph

Figure 9: Packet number 926 was sent at 5.123 second

Figure 10: Packet number 18805 was sent at 67.68 second

Figure 11: assignment2-tcp-4-b-4 Window Scaling Graph

Figure 12: Packet number 926 was sent at 5.123 second

Figure 13: Packet number 18805 was sent at 67.68 second

        Q4-b-5) I have made an ftp request to gaia.cs.umass.edu.wireshark-labs/alice.txt

        to download the file alice.txt. According to Time Sequence Stevens Graph at 1.334

        second, packet number 13 was sent and at 1.564 second packet number 25 was sent.

        Number of packet sent per second as a rate in time interval 1.334 to 1.564 is approximately 19.

        If we look, at 1.789 second sent packet number was 51 and 2.088 second sent packet

        number was 75 . Number of packets sent per seocnd as a rate in time interval

        1.789 to 2.088 is approximately 67 so we can see that packet sending rate started

        at slower rate and it has increased gradually. This indicates slow start behaviour.

        Same behavior can be seen in Window Scaling Graph. Also when we look at the

        window size it has increased gradually in certain time intervals in response to

        increased number of sent packets.

Figure 14: ftp request made to gaia.cs.umass.edu to fetch alice.txt file

Figure 15: assignment2-tcp-4-b-5 Time Sequence Stevens Graph

Figure 16: Packet number 13 was sent at 1.334 second

Figure 17: Packet number 25 was sent at 1.564 second

Figure 18: Packet number 51 was sent at 1.789 second

Figure 19: Packet number 75 was sent 2.088 second

Figure 20: assignment2-tcp-4-b-5 Window Scaling Graph

Figure 21: Packet number 13 was sent at 1.334 second

Figure 22: Packet number 25 was sent at 1.564 second

Figure 23: Packet number 51 was sent at 1.789 second

Figure 24: Packet number 75 was sent 2.088 second

        -UDP SECTION-

        I have created a scenerio in which I made a DNS query for iyte.edu.tr domain

        name with dig tool which can be used for making DNS queries from terminal

        in Linux. As DNS uses UDP as an underlying transport layer protocol we can

        analyze UDP packets send and recevied as well in this scenario.

        Q1-) Destination IP address of the sent packet is 192.168.166.10. It is not

        possible to be sure that packet reaches to destination address because UDP

        does not use any acknowledgement mechanism. Packet may be lost and we

        can never know this because of unavaliable acknowledgement mechanism.

Figure 25: Destination IP address of sent UDP packet
        Q2-) Source port number for sent packet from my host is 56502, and

        destination port number is 53. For received packet as a reply to this packet,

        source port number is 53, and destination port number is 56502. Source and

        destination port numbers are reverses of each other for the sent and received

        packet.

Figure 26: Source and destination port numbers for sent packet

Figure 27: Source and destination port numbers for received packet as a reply

        Q3-) UDP header size is 8 bytes and UDP payload size is 29 bytes for packet

        sent from my host. For the received packet header size is same which is 8 bytes

        and payload size is 45 bytes. UDP header consists of 4 fields, 16 bits for source port

        number, 16 bits for destination port number, 16 bits representing total length (header

        plus data) and 16 bits for checksum.

Figure 28: Header and Payload size for sent packet

Figure 29: Header and Payload size for received packet

        -UDP Header Structure-

        16 bits 16 bits

    Source Port
 Destination Port

        UDP Header

        Length
     Checksum

        Q4-) Checksum value of the packet sent from my host in hexadecimal

        notation is ce9a (1100111010011010 in binary). Checksum value of the

        of the packet received as a reply in hexadecimal notation is a9ae

        (1010100110101110 in binary). Packets sent via UDP may become

        corrupted while transmission. To check whether information is accurate

        or not checksum values are used.

Figure 30: Checksum value for the packet sent from my host
Figure 31: Checksum value for the packet received from iyte.edu.tr